## Slide 1: Embedded C program for interfacing a LED and switch with STM32

## Slide 2: Objectives
Read the status of the switch.
If the switch Is on, turn on the LED.
If the switch is off, turn off the LED.

## Slide 3: Steps for programming STM32
Enable clock for necessary ports.
Reset the GPIO’s that are to be used.
Configure the GPIO’s for input/ output.
Reset the PUPDR register for necessary pins.
Configure the necessary pins for PULL UP/ PULL DOWN with PUPDR.
Read necessary IDR values and actuate peripherals by configuring necessary ODR’s.

## Slide 4: Enabling Clock
RCC->AHB1ENR = 0X00000001;
Let us use GPIOA for all the operations

## Slide 6: How to Write a value into a register?
GPIOA->MODER = 0X00000001; //which means PA.0 is output
Now if I want PA.3 to be as output then
  GPIOA->MODER = 0X00000040;
  This will configure PA.3 as output but remove the previous configuration of PA.0.
Instead we can use “&=~” combination read as “and assigned with negation of” to reset necessary ports.
We can use “|=“ combination read as “or assigned with” to configure to required mode.

## Slide 7: How to Write a value into a register?
Objective: make PA.0 as output and PA.1 as input
Steps:
  Reset the MODER register of port A pertaining to PA.0 and PA.1.
    A moder state of “00” for a particular pin is assumed to be the reset state.
    GPIOA->MODER&=~0X0000000F;
  Configure the MODER register of port A for PA.0 as o/p and PA.1 as i/p
    “01” for a pin is treated as output.
    “00” for a pin is treated as input.
    GPIOA->MODER |= 0X00000001;

## Slide 9: Configuring pull up and pull down registers
Why should I configure PUPDR?
  When I don’t press the switch, the default value of the switch is depended on whether the pin is pulled up or pulled down.
What are the default values?
  Pulled up pin: Default value is “0”.
  Pulled down pin: Default value is “1”.
  “00” is for No pull up No pull down
  “01” is for Pull-Up
  “10” is for Pull-Down
  “11” is Reserved
Reset PUPDR
  GPIOA->PUPDR&=~0x0000000C;
Configure PUPDR
  GPIOA->PUPDR|=0X00000004

## Slide 10: Monitoring IDR
Read data from IDR
  First construct the monitoring bit, here IDR1 must be 1 to monitor the state of IDR1 we have to perform bitwise and with IDR register
  Flag = GPIOA->IDR & 0X00000002;

## Slide 11: Configuring ODR
Make the respective ODR of PA.0 which is ODR0 as “1” if flag is 0 (pulled up pin)
If(!flag)
  GPIOA->ODR |=0X00000001;
else
  GPIOA->ODR |=0X00000001;

## Slide 12: Final Code

## Slide 13: Please Subscribe to my channel……..
Like Share Comment Subscribe